## Slide 1: Spike sorting in Spike2 Korey Kam 6/7/2016

## Slide 2: Overview
Definition of a spike
Artifacts in freely behaving mice
Detection
Processing events
Export to MATLAB
Processing events with drug injections

## Slide 3
Definition of a spike
Cross channel (>2)
  Waveform shape
    Simple (single positive to negative deflection within 200 ms window)
    Complex (multiple positive to negative deflections, within 200 ms window)
Single (generally HC only)

## Slide 4: IIS (cross channel, simple)

## Slide 5: IIS (cross channel, complex)

## Slide 6: Focal spikes

## Slide 7: Focal spikes (HC only)

## Slide 8: Procedure (manual)
10 sec epoch view
Autoscale Y-axis (check button)
Add marker
Play realtime

## Slide 9
ARTIFACTS in freely behaving mice
Jumping
Head scratch
Sleep to wake
Grooming
Chewing
Injection

## Slide 10: Types
Jumping
Head scratch
Sleep to wake
Grooming
Chewing
Injection

## Slide 11: Jumping
Notes: 10 sec

## Slide 12: Jumping (1min)

## Slide 13: Head stage scratch

## Slide 14: Head stage scratch

## Slide 15: Sleep to Wake

## Slide 16: Grooming

## Slide 17: Chewing

## Slide 18: Injection/scruffing

## Slide 19
DETECTION

## Slide 20: Why use Spike2?
Template vs. threshold only: Spike 2 has built-in powerful methods of spike detection and sorting (spike shape discrimination).
Semi-automated: It took me about 5 min to detect your spikes while rejecting the artifacts using the simplest method: template-based sorting.

## Slide 21: Why look at waveform?
Waveforms can identify a characteristic potential change that may be linked to noise, artifacts, or biologically consistent events.

## Slide 22: Spike Detection Overview
Manual detection
Automated detection
Create multichannel event templates (spikes & artifacts)
Search through recording w/ templates
Mark events
PCA  K-means clustering
Quality control
  Manual verification
  Reclassify events
  Re-mark events
Analysis of events
Export to mat
Notes: Create multichannel event templates (spikes & artifacts)
Search through recording w/ templates
Mark events
PCA  K-means clustering
Quality control
  Search marked events with active cursors (manual)
  Reclassify events to templates
  Re-mark recording
Analysis of events
  Waveform analysis
  Spike width
  PSTHs
  Cross correlations
  Interval histograms
  Rate displays
  Mean and instantaneous frequencies
Separate wavemarks: use Average N

## Slide 23: N-trode
Select channels  analysis tab  New N-Trode

## Slide 24: Create window: -50 to 150 ms

## Slide 25: Make Templates: Overview
Compute threshold  script
Save measurements
Run event detection

## Slide 26: Make templates:
NtrodeNew Wavemark (semi-supervised)
Set thresholds per channel (run kk_4trodesetthresh script)
Track cursor 0
Jump to start
Set duration to -50 to 150 ms
Enable overdraw and “show template limits”
P to play, V to stop
When template created, drag spikes. Make a template for artifacts as well so that they do not contribute to IIS templates.
Cycle through once, then reintialize counters. Make sure to lock template shapes then “Jump to Start.”
Uncheck box “make templates”. We have already created them.
Count and add as wavemark data channel.
Print waveforms.
Verify counts by marker filter  wavemark drawmode Lines Sum in XY measurements

## Slide 27: Set template parameters

## Slide 28: Save templates as a channel

## Slide 29: If no templates, make parameters more stringent
If no spikes, either supervised template forming or change Number of similar spikes from 8 to 4

## Slide 30: Construct Templates
Run for 1-4 hrs to allow event templates to be made for rare spike waveforms
Notes: Script:
Calculation of mean but a high-pass filter set for the waveforms passed into the spike shape dialogs, so the waveform has a mean level of 0 as seen by the dialog.
SD: use levels as variable to set thresholds to.
Scale: If any of your channels had a negative scale factor, then you would be setting the trigger levels in the wrong direction. If you do this, then the dialog sets the level to 0.
SSRun() optional: If you want the dialog to run through your data before moving to the next channel you need to set non circular replay mode and then position the replay to the start, use SSRun() then wait for the cursor position to reach the end in a loop that allows the system to idle (i.e. Interact, Toolbar, use a dialog or use Yield().

## Slide 31: Event templates

## Slide 32: Example templates
Notes: From mEEG268 070313

## Slide 33: Select PCA

## Slide 34: From events to principal components

## Slide 35: Clear clusters

## Slide 36: Perform Kmeans clustering

## Slide 37: Cluster PCA with Kmeans

## Slide 38: Apply PCA to wavemark channel

## Slide 39: Remove artifacts via PCA & Kmeans
Change marker filter to all codes.
AnalyzePCA
All traceswaveformsOK
Form cluster centers
  Clear all codes
  Switch to density
  L-click, place user ellipse, Small ellipse
Kmeans from existing, use existing clusters
Apply changes
If satisfied, copy cluster values

## Slide 40: Example PCA templates (spikes and artifacts)

## Slide 41: Spike sorting (PCA)

## Slide 42: Refinement with PCA

## Slide 43: Filter by code

## Slide 44: After PCA: filter out artifacts by spike code
Change marker filter to only spike codes.
Reclassify events to spike code.
Verify using Edit Wavemark dialog and Overlay.
Verify using 0 cursor tracking.

## Slide 45: PCA refinement: Results

## Slide 46: Make 2nd PCA sort

## Slide 47: After PCA 2x: refine by filtering spike codes
Change marker filter to all but artifacts.
Reclassify events to spike code.
Any new events that are classified as artifacts can be removed.

## Slide 48: Display Principal Components

## Slide 49: After templates made: count true spikes
Copy as memory channel.
Change channel draw mode to lines.
Count using X-Y method

## Slide 50: Add tick marks to detected spikes

## Slide 51: Counting Marked spikes

## Slide 52
Processing

## Slide 53: Labeling IIS peaks (prior to counting/ISIH)
Select wavemark channel
Analysis  Memory Buffer  Create New Buffer
Buffer Type “Event-”  Import…
Min Interval = 0.5, Size = threshold ~40 uV or computed threshold crossing
Write All Memory Channel
Rename “Peaks”

## Slide 54: Single channel peaks
Compute AverageNtrode waveforms (separates 4 channel spikes to individual spikes)
Create New Buffer channel (peaks find) for each spike channel
Write all to memory buffer

## Slide 55: Searching marked events
Use active cursor search mode
Right: control+shift+
Left: control+shift+

## Slide 56: Iterations
Repeat PCA-kmeans clustering until all clusters are true spikes (2-3 iterations)

## Slide 57
EXPORT to mat

## Slide 58: For spike timestamps, do not bin

## Slide 59: For EEG data

## Slide 60
DRUG studies

## Slide 61: Drug studies: set injection times
Set cursor X to time of injection
Create new buffer channel
Buffer type = TextMark, 32 char. Hit OK
Right click on channel, Add Items
Select Buffer channel, Select Cursor (0).
Type description in TxtMark string(drug IP). Hit Add.
Add other textmark items if necessary.
When done, write all memory buffer of the memory channel (Ch TYPE = TextMark).
Go to View, Vertical Marker. Adjust settings.

## Slide 62: Drug studies: histogram of IIS
Use WaveMark Measure script.
Source to count: IIS event channel
Measurement: Sum
Start time: Cursor 1 (inject, baseline)
End time: X hours post drug
Plot results

## Slide 63: Change in spike shape post-drug treatment
PCA
Time axis view to show drift?
Another advantage of the PCA clustering is that it gives you tools to handle drifting spikes. One tool is to use time as Z axis (keyboard shortcut T, or use the button
on the toolbar). Then press X to ensure that the image is properly oriented, and you will have time running from left to right in the window
There is yet another method of handling drifting spikes in the PCA clustering window.
With Time as Z enabled, press Z. Now you are looking along the Z axis, which is time axis. Enable time range (View>Show time range) and you will see only spikes
within certain percentage of your time range (you can set the percentage). By moving the slider you can observe how your cluster (or clusters) of drifting spikes crawl to
different locations in the PCA space. Use the >> and << buttons to animate it and follow the movement of the cluster. Once you know where it is and where it has
moved, you can move in time stepwise with the slider and use the ellipse or user-defined shape to encircle the cluster of real spikes at each time period and apply a code.

## Slide 64: TIFFs of drug effect
Set 0 cursor to hit on injection times in Textmark channel

## Slide 65: Light vs Dark Count
Find Seconds @ 19:00:00 = 7:00 PM
Find seconds @ 1:7:00:00 AM
12 hrs = 43200 seconds

## Slide 66
OLD STUFF

## Slide 67: Example results

## Slide 68: Marking IIS

## Slide 69: Identify IIS (cross channel events)
Select wavemark channel
Analysis  Memory Buffer  Create New Buffer
Buffer Type “Event-”  Import…
Min Interval = 0.2 sec, Level = threshold 49 uV
Write All Memory Channel
Rename “IIS”

## Slide 70: Separate Ntrode traces
Get channel info. Points=532, Pretrig=171, Traces=4

## Slide 71: Event correlation
FC-OC
FC-RHC

## Slide 72
PERFORMANCE

## Slide 73: Automated detection of interictal spikes w/ artifact rejection
EC
FC
LHC
RHC
How?
With waveform shapes based on templates and amplitude thresholds

## Slide 74: Spike Detection Performance
Chart: True Positive Ratio
| Manual | SD 3 | SD 5 | SD 6 | SD 7 | SD 8 | SD 10
Manual SD 3 SD 5 SD 6 SD 7 SD 8 SD 10 | 1 | 1.2461 | 0.80859 | 1.1641 | 1.0898 | 1.1133 | 0.55859
Validated on long recording (19.4hrs) of 5.6 wk old Tg2576 male

## Slide 75: Diurnal Cycle of Spikes
Chart: Spike Fraction
| Light | Dark
Light Dark | 0.76329 | 0.23671
Chart: No. of Spikes
| Light | Dark
Light Dark | 158 | 49
Validated on ON recording (19.4hrs) of 5.6 wk old Tg2576 male

## Slide 76: Waveforms
Movement-related Artifacts
Interictal Spikes
Overlay
EC
FC
LHC
RHC
Validated on ON recording (19.4hrs) of 5.6 wk old Tg2576 male

## Slide 77: Average waveform
Waveform Ave (black)+ SD (red)
Filters: none
Time: 0 to Max
0.25s bins
Trigger on self
Notes: Yes, you can do it, but after you apply your clustering to the data file. In the time view which holds your spike channel, use Marker Filter to select your first spike. Then go to Analysis > New result view > Waveform average and set: Channels AND Trigger to your spike channel, Width to the length of a single spike trace in seconds (I'll get back to it), Offset to 0, Align data to "Next data point", Display mean of data and Error bars to enabled. "Keep item count" does not matter in this case. Press New. In the next dialog (Process dialog), select the time range of in your file over which you want to average the spikes; normally it would be 0 to the end of file. For the end of file use MaxTime(), but the dialog should default to the entire file (expressed as the number of seconds) anyway. Use Process all data and Optimise display. Clear result may be needed if you re-do the analysis in the same window. Press Process. You should get your mean waveform, but with SEM instead of SD. Right-click on it, select Channel draw mode and change error to SD. If you want a smoother-looking trace, change the drawing mode from Lines to Cubic Spline. You may need to optimise the Y axis to accomodate the SD lines. Press Ctrl+Q or right-click on the Y axis and go to Y axis range > Optimise. I think this is the closest you can get in Spike2, with the +/-SD range shown as two lines instead of colored area. Now go back to your time view, use the Marker Filter to select another spike, and repeat the process. And here is how to figure out the length of a single spike trace. One method is to zoom in on a single spike, and use two cursors and Cursor Regions windows to measure it manually. Another one is to click on the data file (to ensure it is the current view), then go to Script>Evaluate, enter BinSize(1)*MarkInfo(1) (instead of the 1s, use the channel number of your spike channel) and click on Eval(...).

## Slide 78: Detect Peaks
Detect peaks of wavemark data. (Create New Buffer Channel)
Buffer Type = Event-
Mode = Peaks
Min interval = 0.5 sec
Size = 5 uV

## Slide 79: Inter-Spike Interval Histogram
From peak located event channel.
AnalysisNew Result ViewInterval Histogram
Channel = Peak labeled
Width = 60 sec
Bin size = 1 sec
Min interval = 0

## Slide 80: PCA
K means clustering = 3

## Slide 81: Spike Width
Roughly speaking you first set up cursor 0 so it iterates from spike to spike, then set up other active cursors that find the relevant locations starting from cursor 0. So you might set cursor 1 to find the spike peak, cursor 2 to find the start of the spike and cursor 3 to find the end. These last two will be the difficult ones - you may have to use two more cursors to find the steepest rising & falling slope, then search out from those positions using slope percentage searches to find when the slope drops to 20% of the maximum. Once the cursors are set up you can create your XY view and generate the measurements to it pretty simply - so the amplitude is level at cursor 1 - level at another cursor using the value difference measurement, duration is a time difference measurement and area is a curve area measurement. You can save your active cursor settings using File : Resource Files : Save resources as and they can then be applied to another file using File : Resource Files : Apply resource file.
http://www.ced.co.uk/phpBB3/viewtopic.php?f=13&t=1204

## Slide 82: Spike Width
http://www.ced.co.uk/phpBB3/viewtopic.php?f=13&t=1204

## Slide 83: Spike Analysis

## Slide 84
Spike detection and sorting Spike2 identifies and sorts single and multi-unit activity both on-line and off-line. It can mark events using simple threshold crossings or sort up to 32 channels on-line with whole wave spike shape template matching.
For multi-unit recordings, Spike2 contains tools for sorting spikes based on the spike waveform shape. All events crossing a threshold are captured. A combination of template matching and cluster cutting based on Principal Component Analysis (PCA) or user-defined measurements is then used to sort spikes into different units
The template matching system allows templates to be fixed or to track changing spike shapes. Templates can be created automatically or by manual selection of individual spikes.
Cluster cutting methods plot measured values into a 3D view that can be rotated and replayed to show the occurrence of the spikes through time. Clusters are formed by automatic algorithms or manually by placing ellipses. Interactive features include INTHs for current cluster classes, tracking over time, and selection of an individual spike by clicking on its dot in the cluster.

## Slide 85: EXPORT smr post8hr
Time (s) = cursor + 3600*8
Time shift to 0
Set big file

## Slide 86: Stage/Counts
After export, check PCA spikes
Sleepscore to get spectral power
Zscore wideband power
Stage with video/movement

## Slide 87: Timestamps from Spike2: make “events” file
Do not align and bin event channels

## Slide 88: Separate channels (averageNtrode script)
Select PCA sorted channel
Execute AverageNtrode script
Find peak times in memory buffer, call channel “spikeX”
Write buffer to file

## Slide 89: Separate channels: make timestamps (events)
Make Events channel using “Peaks” of wavemark channel with horizontal cursor

## Slide 90: Separate spike channels: export to matlab as TIMESTAMPS vector
load('417_7mo_spikeTimes.mat') at roughly 7kb

## Slide 91: Separate channels (crosschan script)